## Slide 1: Reserve Design in the Sandhills
Matthew Moskwik

## Slide 2: Our Current Reserve Design

## Slide 3: Advantages of Utilizing Conservation Planning Software
Combine all important features
  Create targets for each
  Assign weights/rankings to inputs
Use county parcel data as selection units
  Assign costs and/or size limits
Create boundary penalty
  Produces more compact reserve
Result: Prioritizes landscape for conservation action with known constraints

## Slide 4: Setup for a Simple Purchase-only Model
Set targets for features

## Slide 5: 1. Set Targets for Features
Name | Amount | Ratio | Target
Other Element Occurrence | 23914.93 | 0.75 | 17936.2
Other Managed Area | 143065.5 | 0 | 0
NHPNA | 905491.3 | 0.95 | 860216.8
NHPNA Candidate | 14609.19 | 0.75 | 10956.89
RCW Active Foraging Area | 515708.6 | 0.95 | 489923.2
Floodplain | 273679.7 | 0.25 | 68419.94
RCW Inactive Foraging | 176481.6 | 0.5 | 88240.82
Potential Upland | 348139.8 | 0 | 0
Restoration Area | 66780.55 | 0.5 | 33390.28
Smoke Awareness | 181236.6 | 0.25 | 45309.15
Stream Buffer | 573330.7 | 0.25 | 143332.7
Wildlife Connector | 135024.1 | 0.75 | 101268
Brownwater Levee Hardwood Forests | 173.9058 | 0.5 | 86.9529
Cypress-Gum Swamp Forests | 23549.59 | 0.5 | 11774.79
Dry-Wet Hardwood and Mixed Forests | 150467 | 0.5 | 75233.5
Dry-Hydric Hardwood and Mixed Forests | 23721.96 | 0.5 | 11860.98
Forest Canebrakes | 156487.6 | 0.5 | 78243.81
Forested Floodplains | 161191.9 | 0.5 | 80595.97
Forested Floodplains and Non-Riverine Wet Flats | 9274.43 | 0.5 | 4637.215
Pitcher Plant Meadows and General Wet | 500.592 | 0.5 | 250.296

## Slide 6: Setup for a Simple Purchase-only Model
Set targets for features
Format parcel data
  Identify protected areas

## Slide 8: Setup for a Simple Purchase-only Model
Set targets for features
Format parcel data
  Identify protected areas
  Exclude areas from analysis (i.e., cities, sand mines)
  Establish costs: number of acres

## Slide 9: Setup for a Simple Purchase-only Model
Set targets for features
Format parcel data
  Identify protected areas
  Exclude areas from analysis (i.e., cities, sand mines)
  Establish costs: number of acres
3. Create boundary penalty
  Moderate penalty assigned for this example

## Slide 10: Trade-off between Reserve System Boundary Length and the Total Area of the Reserve System

## Slide 12: Advanced Setups
Protection can have multiple categories (aka zones)
  Different costs and conservation values assigned to each zone
  Lock-in properties to specific zones
  Properties can move between zones
    Assign costs when movement occurs

## Slide 13: Example: Purchase or Easement
Easement ¼ the cost of purchase
Only ½ of conservation value in easement
Current easements can be purchased at full cost to reach targets or remain at no cost, but remain at ½ conservation value

## Slide 16: Interest in Implementing?
Decide upon simple or advanced setup
One meeting to decide upon values for model parameters
A second meeting to review results